## Slide 1: Flashing RIOT from a Browser
Presentation by Fabio Lehmberg and Jakob Fregin
Dresden, 26.03.2026

## Slide 2: Vision

## Slide 3: Vision
open a website
write your RIOT code
connect and flash your device
no setup
    toolchain
    IDE
no platform dependecy
Notes: Stellt euch vor
website aufmachen
RIOT code schreiben
dann direkt einfach builden und flashen
kein setup
platformunabhängig

## Slide 4: Goals

## Slide 5: Goals
flash RIOT boards from a browser
provide a code editor as a website
ready-to-use development environment
ease-of-use for newcomers
keep to a RIOT native user experience
ease-of-deployment
Notes: Ziele im Rahmen unseres Projektes
geräte von einem Browser flashen
fertiges dev env mit editor
shortcuts für Anfänger
möglichst nah an RIOT bleiben
einfache lokale Benutzung
oder auch zentrales hosting

## Slide 6: How to flash an MCU from a Browser?

## Slide 7: How to flash an MCU from a Browser?
APIs: WebUSB, WebSerial, WebHID
    limited device access
    support by chromium-based browsers only
    serial flashing is most common
  flashing a device with WebSerial
    still requires flasher logic in js
    device dependend
    implementing your own flasher is not trivial
Notes: WebSite lässt keine direkte kommunikation mit geräten zu
deswegen APIs
so kann man zB auf USB Serielle oder HID geräte zugreifen
diese APIs werden allerdings nicht von allen Browsern gleich unterstützt
so wird WebSerial (was wir zum flahsen brauchen) nur auf chromium basierten browsern unterstützt
darüberhinaus ist web zugriff auf HW devices ein großes Sicherheitsrisiko
weshalb man jedes Gerät einzeln zulassen muss
nun wenn man mit einem µC seriell kommunizieren kann,
benötigt man immernoch einen flasher der impl in js, die compileten binaries auf den µC überträgt
hängt vom device ab -> mehrere flasher
eigene flasher zu schreiben ist nicht praktikabel
flashing websiten existieren, ABER:
für spezifische devices
muss seine eigenen binaries hochladen
nicht für alle geräte und wenn verteilt
können immernoch keinen eigenen Code schreiben, könn wir nicht iwie einen Editor hosten in dem wir auch flashen können

## Slide 8: What about web hosted code editors?

## Slide 9: What about web hosted code editors?
  coder/code-server:
    Monaco style editor (VSCode)
    familiarity
    extension support
    flexible deployment
  idea: vscode-extension for flashing devices
    can be automatically deployed in the dev env
    allows for editor-integrated management of devices
    automatically flashes binaries from your built code
Notes: ham uns web IDEs angeguggt
viele haben Monaco als Frontend, bekannt von VSCode
VSCode für viele vertraut
unterstütz Extensions
coder/code-server kann einfach gehosted werden um eine Web IDE bereit zustellen
IDEE: vscode extension zum flashen
auto deploy
geräteverwaltung
in Kontrast zu anderen Flasher Websites -> seinen code direkt builden und flashen

## Slide 10: Backend

## Slide 11: Goals Reminder
provide a code editor as a website
ready-to-use development environment
keep to a RIOT native user experience
ease-of-deployment
flash RIOT boards from a browser
ease-of-use for newcomers

## Slide 13: Architecture

## Slide 14
RIOT Web Editor Architecture
Notes: frontend:
  Vsccode ext
  Commadlines
backend:
  code-server
  nutzer input in cli
  viele CLIs – eine extension -> relay (EINE CONNECTION, zentraler host)
  erlaubt buttons -> command shortcut -> command sichtbar
  2 fragen offen:
    Kommunikation Shell – WebExtension
    Stub

## Slide 15: Protocol
Requirements:
    Buttons issue commands (Client -> Shell)
    Commands are sent to Client
    Log messages and User Input are shared
  human-readable and compact
  stateful, addressed -> parallelism
Notes: Mischung: Human + compakt
mehrere geräte, mehrere shells -> parallel
stateful -> WS + registrieren Addressen
Struktur:
  typ
  sender
  empfänger
  payload felder
    hier Flashcommand

## Slide 16: Stub
Why?
    make flash -> parsable
    ./my_flash_script.sh -> more difficult
    ./my_flash_tool.bin -> impossible
  Solution:
    patch riot slightly -> adjust make targets to call a stub instead
    stub is called as flasher or serial tool with their respective args
    stub communicates with the client:
      invokes commands
      displays output
      relays user input
Notes: parsing problem
patch riot
call stub
commands zum Client
output anzeigen
input an CLient

## Slide 17: Packaging and Deployment

## Slide 18: Docker
package into a docker image, containing:
    code-server (autostart)
    riot-web-tools:
      relay (autostart)
      shell (default shell for code-server)
      stub
    RIOT and its dependencies
    user environment /home/coder

## Slide 19: Limitation

## Slide 20: Limitations
web APIs are very constricted
confined VSCode web extension context
device support has to be added manually (flasher.js + make patch)
some devices still require a driver to be recognized by your os
1 container – 1 user
Notes: Gerätezugriff durch Web APIs ist erschwert
VSCode Web Extensions an vielen Punkten (aus Sicherheitsgründen) beschränkt
Neue Geräte müssen manuell eingebaut werden -> flasher + make
Treiber

## Slide 21: Features / Support

## Slide 22: Features / Support
flash and term via:
    UI
    CLI
  coherent UI / CLI experience
  multiple devices and projects
  boards:
    adafruit-nrf52840 (RIOT kit)
    esp (all)

## Slide 23: Demo
Notes: default workspace
open shell project
add esp32 (hello world)
flash esp32
term (offen)
add adafruit (shell)
flash
term
cd timer
make by keyup

## Slide 24: Thanks for your attention
RIOT-Web-Editor:
https://github.com/cheater78/RIOT-WebEditor
RIOT-VS-Code-Extension (Submodule)
https://github.com/Barkolores/RIOT-VS-Code-Extension

## Slide 26: Shell

## Slide 27: Relay